## Slide 1
Dr. B.R. Ambedkar National Institute of Technology Jalandhar
Jalandhar(144008), Punjab
Password Lock FSM
Submitted to: Submitted by:
Group 6
Dr. Tarun Chaudhary Aditya (25904138)
Assistant Professor, ECE Mayank Verma (25904145)
NITJ, Jalandhar Sarthak Singhal (25204131)
Karthikeyan (25904141)
Pradhum Kumar (25904147)

## Slide 2: Abstract
This project demonstrates how FSMs can create robust security applications with features like:
4-digit password entry system
Failed attempt tracking (3 attempts before lockout)
Automatic timeout reset
Timed unlock duration
Password change capability
Helps understand how to architect a state machine that handles complex sequential logic and security protocols.

## Slide 3: Password Lock FSM
Password Lock FSM is a security mechanism that grants access to anything like device or may be doors/ lockers cars etc. only when the correct password is entered.
Widely used in digital security systems like electronic safes, electronic door locks, and embedded devices.
It ensures protection against unauthorized access.
At the heart of these systems lies a simple yet powerful concept:
Finite State Machine (FSM).

## Slide 4: Finite State Machine
A Finite State Machine is a sequential logic model used to design systems that operate through a series of well-defined states. The system moves from one state to another based on input signals and predefined rules.
FSM consists of a finite number of states.
The system can be in only one state at a time.
State transitions occur when specific inputs or conditions are met.
Used to design control-oriented digital systems.

## Slide 5: How FSM Works

## Slide 6: Types of FSM
Mealy Machine
Moore Machine

## Slide 7: Why use FSM for Password Lock
FSM allows stepwise verification of input digits
Ensures deterministic behavior
Reliable for embedded security applications
Easy to Handle Wrong Inputs.
Supports Reset and Retry Logic
Simplifies Debugging and Simulation

## Slide 8: System Architecture
1. Input Interface
Digit Input (4-bit)
Enter Button
Change Password Button
2. Edge Detection Module
Detect a clean rising pulse from the enter button.

## Slide 9: System Architecture
3. FSM Controller
This is the core of the system.
States
IDLE: Initial locked state, waiting for first digit
DIGIT1-DIGIT4: Sequential digit entry states
CHECK_PASSWORD: Validates entered password against stored password
UNLOCKED: Door unlocked for 10 seconds
WRONG_PASSWORD: Increments failed attempt counter
LOCKED_OUT: System locked after 3 failed attempts
TIMEOUT: 30-second penalty before returning to IDLE
CHANGE_PASSWORD: Special mode for updating password
Responsibilities:
Controls system behaviour.
Moves sequentially from digit 1 → digit 4.
Triggers password checking.
Decides lock/unlock/error states.

## Slide 10: System Architecture
4. Password Storage & Handling
a) Stored Password
b) Entered Password
5. Password Comparison Block
A parallel comparator checks the input and outputs
6. Attempt Counter Logic
Counts wrong attempts.
Max allowed attempts = 3.
7. Output Control Unit
Controls external indicators

## Slide 11: Working
Top-level: An FSM implementing a 4-digit digital lock.
Inputs: clk, reset, digit_in (0–9), enter_btn, change_pwd_btn
Outputs: led (status), seg/an (7-seg), locked (1 = locked, 0= unlocked).
States: IDLE → DIGIT1 → DIGIT2 → DIGIT3 → DIGIT4 → CHECK_PASSWORD → UNLOCKED (or WRONG_PASSWORD / LOCKED_OUT).
DIGIT4 automatically proceeds to CHECK_PASSWORD.
Password storage: password[0:3] initialized to 1,2,3,4. Entered digits saved into entered_digits[0:3] on rising edges of enter_btn when in the corresponding DIGIT state.
Button edge detect: two-flip flop sampling of enter_btn creates enter_btn_rising (rising edge detection).
Password check: combinational compare of all four entered digits to stored password.
Attempt counting: attempt_count is intended to track failed tries and move to LOCKED_OUT after 3 attempts.

## Slide 12
IDLE /
LOCKED
DIGIT 1
DIGIT 2
DIGIT 3
DIGIT 4
CHECK PASSWORD
UNLOCKED
LOCKED OUT
WRONG
PASSWORD

## Slide 13: Security Features
Attempt Limiting: After 3 incorrect passwords, the system enters LOCKED_OUT state
Timeout Protection: Automatic reset if user takes too long between digits
Timed Unlock: Lock automatically re-engages after 10 seconds
Password Management: Secure password change mode with verification

## Slide 14: Code
module digital_lock ( input wire clk, input wire reset, input wire [3:0] digit_in, // Input digit 0-9 input wire enter_btn, // Button to submit digit input wire change_pwd_btn, // Button to change password output reg [15:0] led, // Status LEDs output reg [6:0] seg, // 7-segment display output reg [7:0] an, // 7-segment anodes output reg locked // Lock status (1=locked, 0=unlocked) ); // STATE DEFINITIONS localparam [3:0] IDLE = 4'd0; localparam [3:0] DIGIT1 = 4'd1; localparam [3:0] DIGIT2 = 4'd2; localparam [3:0] DIGIT3 = 4'd3; localparam [3:0] DIGIT4 = 4'd4; localparam [3:0] CHECK_PASSWORD = 4'd5; localparam [3:0] UNLOCKED = 4'd6; localparam [3:0] WRONG_PASSWORD = 4'd7; localparam [3:0] LOCKED_OUT = 4'd8; reg [3:0] current_state, next_state;
// PASSWORD STORAGE reg [3:0] password [0:3]; reg [3:0] entered_digits [0:3]; reg [1:0] attempt_count;
initial begin password[0] = 4'd1; password[1] = 4'd2; password[2] = 4'd3; password[3] = 4'd4; attempt_count = 2'd0; end // SIMPLE BUTTON EDGE DETECTION reg enter_btn_r1, enter_btn_r2; wire enter_btn_rising; always @(posedge clk or posedge reset) begin if (reset) begin enter_btn_r1 <= 1'b0; enter_btn_r2 <= 1'b0; end else begin enter_btn_r1 <= enter_btn; enter_btn_r2 <= enter_btn_r1; end end assign enter_btn_rising = enter_btn_r1 && !enter_btn_r2; // PASSWORD VERIFICATION wire password_correct; assign password_correct = (entered_digits[0] == password[0]) && (entered_digits[1] == password[1]) && (entered_digits[2] == password[2]) && (entered_digits[3] == password[3]); // STATE REGISTER always @(posedge clk or posedge reset) begin if (reset) current_state <= IDLE; else current_state <= next_state; end

## Slide 15: Code
// NEXT STATE LOGIC - SIMPLIFIED (NO TIMEOUT) always @(*) begin next_state = current_state; case (current_state) IDLE: begin if (enter_btn_rising) next_state = DIGIT1; end DIGIT1: begin if (enter_btn_rising) next_state = DIGIT2; end DIGIT2: begin if (enter_btn_rising) next_state = DIGIT3; end DIGIT3: begin if (enter_btn_rising) next_state = DIGIT4; end DIGIT4: begin // Automatically go to CHECK_PASSWORD after storing 4th digit // No need to wait for another button press next_state = CHECK_PASSWORD; end
CHECK_PASSWORD: begin if (password_correct) next_state = UNLOCKED; else if (attempt_count >= 2'd2) next_state = LOCKED_OUT; else next_state = WRONG_PASSWORD; end
UNLOCKED: begin // Stay unlocked (manual reset to test) next_state = UNLOCKED; end WRONG_PASSWORD: begin // Manual return to IDLE for now if (enter_btn_rising) next_state = IDLE; end LOCKED_OUT: begin // Manual return to IDLE for now if (enter_btn_rising) next_state = IDLE; end default: next_state = IDLE; endcase end // DIGIT STORAGE - SIMPLIFIED always @(posedge clk or posedge reset) begin if (reset) begin entered_digits[0] <= 4'd0; entered_digits[1] <= 4'd0; entered_digits[2] <= 4'd0; entered_digits[3] <= 4'd0; end else begin if (current_state == IDLE && enter_btn_rising) begin // When transitioning from IDLE to DIGIT1, store first digit entered_digits[0] <= digit_in; end else if (current_state == DIGIT1 && enter_btn_rising) begin // When transitioning from DIGIT1 to DIGIT2, store second digit entered_digits[1] <= digit_in; end else if (current_state == DIGIT2 && enter_btn_rising) begin // When transitioning from DIGIT2 to DIGIT3, store third digit entered_digits[2] <= digit_in; end else if (current_state == DIGIT3 && enter_btn_rising) begin // When transitioning from DIGIT3 to DIGIT4, store fourth digit entered_digits[3] <= digit_in; end else if (current_state == UNLOCKED || current_state == WRONG_PASSWORD) begin // Clear entered digits after checking entered_digits[0] <= 4'd0; entered_digits[1] <= 4'd0; entered_digits[2] <= 4'd0; entered_digits[3] <= 4'd0; end end end

## Slide 16: Code
// ATTEMPT COUNTER always @(posedge clk or posedge reset) begin if (reset) begin attempt_count <= 2'd0; end else begin if (current_state == UNLOCKED) attempt_count <= 2'd0; else if (current_state == WRONG_PASSWORD) attempt_count <= attempt_count + 1; end end // OUTPUT LOGIC always @(posedge clk or posedge reset) begin if (reset) begin locked <= 1'b1; led <= 16'h0000; end else begin case (current_state) IDLE: begin locked <= 1'b1; led <= 16'h0001; // State 0 end DIGIT1: begin locked <= 1'b1; led <= 16'h0002; // State 1 end DIGIT2: begin locked <= 1'b1; led <= 16'h0004; // State 2 end
DIGIT3: begin locked <= 1'b1; led <= 16'h0008; // State 3 end DIGIT4: begin locked <= 1'b1; led <= 16'h0010; // State 4 end CHECK_PASSWORD: begin locked <= 1'b1; led <= 16'h0020; // State 5 end
UNLOCKED: begin locked <= 1'b0; led <= 16'hFFFF; // All on = unlocked! end WRONG_PASSWORD: begin locked <= 1'b1; led <= 16'h0040; // State 7 end LOCKED_OUT: begin locked <= 1'b1; led <= 16'hAAAA; // Alternating end default: begin locked <= 1'b1; led <= 16'h0000; end endcase end end

## Slide 17: 7-SEGMENT DISPLAY
reg [15:0] refresh_counter = 0;
always @(posedge clk) begin
refresh_counter <= refresh_counter + 1;
end
wire [1:0] mux_select = refresh_counter[15:14];
function [6:0] encode7;
input [3:0] num;
case(num)
4'd0: encode7 = 7'b1000000;
4'd1: encode7 = 7'b1111001;
4'd2: encode7 = 7'b0100100;
4'd3: encode7 = 7'b0110000;
4'd4: encode7 = 7'b0011001;
4'd5: encode7 = 7'b0010010;
4'd6: encode7 = 7'b0000010;
4'd7: encode7 = 7'b1111000;
4'd8: encode7 = 7'b0000000;
4'd9: encode7 = 7'b0010000;
default: encode7 = 7'b1111111;
endcase
endfunction
always @(*) begin
case(mux_select)
2'b00: begin
an = 8'b11111110; // Digit 0 ON
seg = encode7(entered_digits[0]);
end
2'b01: begin
an = 8'b11111101; // Digit 1 ON
seg = encode7(entered_digits[1]);
end
2'b10: begin
an = 8'b11111011; // Digit 2 ON
seg = encode7(entered_digits[2]);
end
2'b11: begin
an = 8'b11110111; // Digit 3 ON
seg = encode7(entered_digits[3]);
end
endcase
end
endmodule

## Slide 18: Testbench
module digital_lock_tb; reg clk; reg reset; reg [3:0] digit_in; reg enter_btn; reg change_pwd_btn; wire [15:0] led; wire [6:0] seg; wire [7:0] an; wire locked; // Instantiate digital lock digital_lock uut ( .clk(clk), .reset(reset), .digit_in(digit_in), .enter_btn(enter_btn), .change_pwd_btn(change_pwd_btn), .led(led), .seg(seg), .an(an), .locked(locked) ); // Clock - 100MHz initial begin clk = 0; forever #5 clk = ~clk; end
// Test initial begin $display("\n========================================"); $display(" DIGITAL LOCK DEBUG SIMULATION"); $display("========================================"); $display("Password: 1-2-3-4"); $display("NO TIMEOUT - Pure state machine test\n"); // Init reset = 1; digit_in = 4'd0; enter_btn = 0; change_pwd_btn = 0; #100; reset = 0; $display("%0t: Reset released", $time); #100; // TEST: Enter password digit by digit $display("\n--- Entering Digit 1 ---"); digit_in = 4'd1; #50; $display("%0t: digit_in = %0d", $time, digit_in); enter_btn = 1; #20; $display("%0t: enter_btn = 1", $time); #100; enter_btn = 0; $display("%0t: enter_btn = 0", $time); #200; $display("%0t: State=%0d, LED=%h, entered[0]=%0d", $time, uut.current_state, led, uut.entered_digits[0]); $display("\n--- Entering Digit 2 ---"); digit_in = 4'd2;

## Slide 19: Testbench
#50; $display("%0t: digit_in = %0d", $time, digit_in); enter_btn = 1; #20; $display("%0t: enter_btn = 1", $time); #100; enter_btn = 0; $display("%0t: enter_btn = 0", $time); #200; $display("%0t: State=%0d, LED=%h, entered[1]=%0d", $time, uut.current_state, led, uut.entered_digits[1]); $display("\n--- Entering Digit 3 ---"); digit_in = 4'd3; #50; $display("%0t: digit_in = %0d", $time, digit_in); enter_btn = 1; #20; $display("%0t: enter_btn = 1", $time); #100; enter_btn = 0; $display("%0t: enter_btn = 0", $time); #200; $display("%0t: State=%0d, LED=%h, entered[2]=%0d", $time, uut.current_state, led, uut.entered_digits[2]); $display("\n--- Entering Digit 4 ---"); digit_in = 4'd4; #50; $display("%0t: digit_in = %0d", $time, digit_in); enter_btn = 1; #20; $display("%0t: enter_btn = 1", $time); #100; enter_btn = 0; $display("%0t: enter_btn = 0", $time); #200; $display("%0t: State=%0d, LED=%h, entered[3]=%0d", $time, uut.current_state, led, uut.entered_digits[3]);
#500; $display("\n========================================"); $display("FINAL RESULTS:"); $display(" State = %0d (should be 6=UNLOCKED)", uut.current_state); $display(" Locked = %b (should be 0)", locked); $display(" LED = %h (should be FFFF)", led); $display(" Password = %0d-%0d-%0d-%0d", uut.password[0], uut.password[1], uut.password[2], uut.password[3]); $display(" Entered = %0d-%0d-%0d-%0d", uut.entered_digits[0], uut.entered_digits[1], uut.entered_digits[2], uut.entered_digits[3]); if (locked == 0) begin $display("\n*** SUCCESS! Lock is UNLOCKED! ***"); end else begin $display("\n*** FAILED! Lock is still locked ***"); $display("Debug info:"); $display(" enter_btn_r1 = %b", uut.enter_btn_r1); $display(" enter_btn_r2 = %b", uut.enter_btn_r2); $display(" enter_btn_rising = %b", uut.enter_btn_rising); end $display("========================================\n"); #10000; $finish; end // Monitor every state change always @(uut.current_state) begin $display("%0t: >>> STATE CHANGED to %0d <<<", $time, uut.current_state); end // Monitor edge detection always @(posedge clk) begin if (uut.enter_btn_rising) $display("%0t: !!! BUTTON EDGE DETECTED !!!", $time); end endmodule

## Slide 20: Schematic

## Slide 21: Simulation Results
4

## Slide 22: Real Life Applications
This FSM design pattern is used in:
Electronic Door Locks: Hotel rooms, office buildings
Safe Systems: Bank vaults, home safes
Vehicle Immobilizers: Keyless entry systems
ATM Machines: PIN verification systems
Access Control: Server rooms, data centres

## Slide 23: Thank You