## Slide 1: 16-bit RISC Processor Design
• Design • Simulation
• Debug • Synthesis

## Slide 2: Overview
  Objective: To Build a simple 16‑bit RISC processor
  Tools: Verilog, Vivado
  Pipeline: Fetch, Decode, Execute, Write‑Back

## Slide 3: Architecture
  Components:
  ALU, ALU Control Unit
  Register File
  Instruction Memory
  Data Memory
  Control Unit
  Data Path Unit
  Pipeline Stages
  16-bit RISC ISA, single-cycle datapath
  Top-level: Risc_16_bit instantiates Control_Unit + Datapath_Unit
  Memory init via $readmemb; simulation in Vivado

## Slide 4: Pipeline Stages
  1. Fetch – Instruction read
  2. Decode – Register file read
  3. Execute – ALU operations
  4. Memory Access – Accesses data memory
  5. Write‑Back – Store results

## Slide 6
SCHEMATIC

## Slide 7: INSTRUCTION SET
  Operations:
  ADD, SUB, AND, OR, NOT
  Right Shift, Left Shift
  LOAD WORD, STORE WORD
  BRANCH instructions
  The instruction set of the RISC processor:
  A. Memory Access Instructions
  1. Load word LW ws, offset(rs1) ws:=Mem16[rs1 + offset]
  2. Store Word: SW rs2, offset(rs1) Mem16[rs1 + offset]=rs2

## Slide 8
  B. Data Processing Instructions
  1. Add: ADD ws, rs1, rs2 ws:=rs1 + rs2
  2. Subtract: SUB ws, rs1, rs2 ws:=rs1 – rs2
  3. Invert (1‘s complement): INV ws, rs1 ws:=!rs1
  4. Logical Shift Left: LSL ws, rs1, rs2 ws:=rs1 << rs2
  5. Logical Shift Right: LSR ws, rs1, rs2 ws:=rs1 >> rs2
  6. Bitwise AND: AND ws, rs1, rs2 ws:=rs1 • rs2
  7. Bitwise OR: OR ws, rs1, rs2 ws:=rs1 | rs2
  8. Set on Less Than:
  SLT ws, rs1, rs2 ws:=1 if rs1 < rs2; ws:=0 if rs1 ≥ rs2

## Slide 9
  C. Control Flow Instructions
  1. Branch on Equal: BEQ rs1, rs2, offset
  Branch to (PC + 2 + (offset << 1)) when rs1 = rs2
  2. Branch on Not Equal: BNE rs1, rs2, offset
  Branch to (PC + 2 + (offset << 1)) when rs1 != rs2
  3. Jump: JMP offset Jump to {PC [15:13], (offset << 1)}

## Slide 10: INSTRUCTION MEMORY
The Instruction Memory stores the program that the processor executes. It outputs the 16-bit instruction corresponding to the current Program Counter (PC) value.
📌 Key Features
16-bit wide ROM
Stores up to 16 instructions (memory[0] to memory[15])
Program loaded from external file (test.prog)
Combinational access → instruction available immediately when PC changes
Addressing uses PC bits [4:1] to index instruction memory
Implements the Fetch stage of the processor pipeline
Allows easy program changes through the .prog file
Provides a clean interface for the Control Unit and Datapath to decode and execute instructions
Helps understand instruction flow inside a simple RISC CPU

## Slide 11: Instructions used (test.prog)
• 0000_000_001_000000 // LW R0 <-Mem(R0 + 0)
• 0000_000_001_000001 // LW R1 <-Mem(R0 + 1)
• 0010_000_001_010_000 // ADD R2 <-R0 + R1
• 0110_000_001_010_000 // logical shift right R2 <-R0>>R1
• 0000_000_011_000010 // LW R3 <-Mem(R0 + 2)
• 0100_011_000_100_000 // NOT R4 <-~R3
• 1000_000_001_110_000 // OR R6 <-R0 | R1
• 1001_000_001_111_100 // Selecton less thanR7 <-(R0 < R1)

## Slide 12: Datapath
  Flow:
  PC → Instruction Memory
  Register Read
  ALU Execute
  Memory Access
  Write‑Back to Register File

## Slide 13: DATA MEMORY
The Data Memory block stores and retrieves 16-bit data during program execution. It supports both read and write operations and is used by load/store instructions in the RISC processor.
Key Features
8 × 16-bit memory array (memory[0] to memory[7])
Synchronous write on the rising edge of clock
Combinational read when mem_read = 1
Address mapped using lower 3 bits (mem_access_addr[2:0])
Memory contents initialized from external file (test.data)
Live monitoring of memory values using $fmonitor for debug/logging

## Slide 14: Control Unit
  Generates control signals:
  ALU Op, RegWrite, MemWrite
  MemRead, MemToReg

## Slide 15: ALU
`timescale 1ns / 1ps
module ALU(
input [15:0] a,b, //src1 AND //src2
input [2:0] alu_control, //function sel
output reg [15:0] result, //result
output zero, Negative, Parity );
always @(*)
begin
case(alu_control)
3'b000: result = a + b; // add
3'b001: result = a - b; // sub
3'b010: result = ~a;
3'b011: result = a<<b;
3'b100: result = a>>b;
3'b101: result = a & b; // and
3'b110: result = a | b; // or
3'b111: begin if (a<b) result = 16'd1;
else result = 16'd0;
end
default:result = a + b; // add
endcase
end
assign zero = (result==16'd0) ? 1'b1: 1'b0;
assign Negative = result[15]; // MSB indicates sign
assign Parity = ^(result); // XOR of all bits → odd parity = 1, even = 0
endmodule

## Slide 16: ALU CONTROL UNIT

## Slide 17: ALU_Control Verilog code `timescale 1ns / 1ps module alu_control( ALU_Cnt, ALUOp, Opcode); output reg[2:0] ALU_Cnt; input [1:0] ALUOp; input [3:0] Opcode; wire [5:0] ALUControlIn; assign ALUControlIn = {ALUOp,Opcode}; always @(ALUControlIn) casex (ALUControlIn) 6'b10xxxx: ALU_Cnt=3'b000; 6'b01xxxx: ALU_Cnt=3'b001; 6'b000010: ALU_Cnt=3'b000; 6'b000011: ALU_Cnt=3'b001; 6'b000100: ALU_Cnt=3'b010; 6'b000101: ALU_Cnt=3'b011; 6'b000110: ALU_Cnt=3'b100; 6'b000111: ALU_Cnt=3'b101; 6'b001000: ALU_Cnt=3'b110; 6'b001001: ALU_Cnt=3'b111; default: ALU_Cnt=3'b000; endcase endmodule

## Slide 18: TESTBENCH
`timescale 1ns / 1ps
`include "Parameter.v"
module tb;
reg clk ;
wire [15:0] result;
initial
begin
clk <=0;
`simulation_time;
$finish;
end
always
begin
#5 clk = ~clk;
end
Risc_16_bit uut(.clk(clk), .result(result),.z_flag(z_flag),.p_flag( p_flag));
endmodule

## Slide 19: Vivado Waveform

## Slide 20: SYNTHESIS and implementation

## Slide 21: Hazards Handling
  Structural hazards avoided
  No data hazards due to simplified design
  Control hazards handled by PC update logic

## Slide 22: outcome
  Working 16‑bit processor implemented
  Reinforced understanding of CPU architecture
  Hands‑on experience with RTL, simulation & synthesis
  Foundation for advanced VLSI/CPU projects

## Slide 23: References
Source: isroset.org https://share.google/KBrFRzuKuID7NFgjf
The Berkeley RISC Project: · Patterson, D. A., & Ditzel, D. R. (1980). "The Case for the Reduced Instruction Set Computer." ACM SIGARCH Computer Architecture News, 8(6), 25-33.2.
The Stanford MIPS Project: · Hennessy, J. L., et al. (1982). "The MIPS Machine." Proceedings of the COMPCON Spring ‘82.
3.The IBM 801 Project (The Predecessor): · Radin, G. (1982). "The 801 Minicomputer." ACM SIGARCH Computer Architecture News, 10(2), 39–47.
Text books:1. Hennessy, J. L., & Patterson, D. A. · Computer Architecture: A Quantitative Approach (Now in its 6th or 7th edition).
M. Morris Mano

## Slide 24: THANKYOU
SUBMITTED TO:
Dr Nitesh Kashyap
Assistant Professor (Grade-I)
ECE, NIT Jalandhar
SUBMITTED BY:
Sathwik 25204132
Aditya 25904138
Vishnu 25904150
M.Tech VLSI Design
1st Semester